Civil Engineer Skills Quiz

Name:

Phone:

Address:

- What are two soil testing Proctors for measuring soil density?

  - What is the difference between the two?

  - What are four components that make up a soil’s matrix?

- In water main design,  what are two factors of the design that can increase flow and reduce losses? What is the “DR” specification and what design element is it relevant to?

- Define the term SWPPP and describe what a SWPPP design includes.

  - Give an example of Structural BMP.

  - What is a vegetative BMP example?

  - What are two BMP’s that can be used in a small drainage way?

  - Who regulates SWPPP?

  - Are inspections required?

- What are three key difference between sediment traps and sentiment basins?

- In pavement design, how do you calculate a required structural number and what test is it based on?

How are geogrids used?

- For the construction of wet sites, list three options for Dewatering.

- Complete this sentence:

  - I found the left turn lane taper in the “Manual on ________________   ___________________ ______________ (MUTCD). Who publishes this engineering standard?

- Turn Lane design is based mostly on ______________.

  - Name the three taper types calculated in left turn lane designs.

- For force main design what design factors influence the calculation of total head?

- What is the benefit of steel rods placed in curb and gutter for truck parking areas?

- For sanitary sewer design:

  - Why are drops needed in manholes?

  - What purpose do clean outs serve?

- What is the Pad Prep note and who writes it for whom?

- What are French drains used for and how do they work?

- Road Design:

  - What is ‘k’ in vertical curve design?

  - What is ‘e’ in super elevation?

  - What is stopping sight distance?

When you complete this quiz, attach it to an email and send it to: Resourceskillsquiz@gmail.com